## Slide 1
HW/SW CODESIGN SEMINAR
Force-Directed Scheduling
for High-Level Synthesis
Mechanism, Comparative Context, and Critical Evaluation
Md Jubair Salehin Razin
Student ID 1230281 · Electronic Engineering, HSHL
Supervisor: Prof. Dr. Achim Rettberg
Notes: <

## Slide 2
1
MOTIVATION
Where scheduling sits in high-level synthesis
Behavioral
description
Scheduling
Binding
RTL netlist
(VHDL entities)
Scheduling assigns every operation to a control step — it fixes the temporal concurrency, and so it largely decides how many functional units the design will need.
Resource-constrained Units fixed → minimise latency
Time-constrained ← FDS Latency fixed → minimise resources

## Slide 3
2
THE CORE IDEA
Balance the resource demand across control steps
FDS treats the per-step resource demand as a system of springs and flattens the peaks — fewer simultaneous operations means fewer functional units, at the same latency.
Peaked (ASAP): 3 multipliers
s1
s2
s3
s4
demand piles into early steps
Balanced (FDS): 1 multiplier
s1
s2
s3
s4
demand spread evenly across steps
Notes: The whole method is one intuition: spread the operations over the slack they have so no single control step is overloaded. Here the three multiplications stop colliding in step 1, so one multiplier suffices instead of three — without changing the latency.

## Slide 4
3
STEP 1 — TIME FRAMES & MOBILITY
ASAP and ALAP bound every operation
Example data-flow graph
v1
v2
v3
v4
v5
× multiply
+ add
Mobility μ(vᵢ) = tL − tS
Op | Type | tS | tL | μ
v1 | × | 1 | 2 | 1
v2 | × | 1 | 2 | 1
v3 | × | 1 | 3 | 2
v4 | + | 2 | 3 | 1
v5 | + | 3 | 4 | 1
μ = 0 means the operation is on the critical path and cannot move; μ > 0 is the slack FDS exploits. Here λ = 4 control steps.
Notes: Step one: run ASAP for the earliest start and ALAP for the latest. The gap is the operation's mobility. v3 has mobility 2, so it can slide; the critical-path operations are pinned. This slack is the raw material the algorithm works with.

## Slide 5
4
STEP 2 — DISTRIBUTION GRAPH
Expected demand on each resource per step
Treat an unscheduled op as uniformly spread over its frame: pᵢ(l) = 1 / (μ+1). Sum per type per step to get DGₖ(l).
Chart: 
| s1 | s2 | s3 | s4
Multiplier | 1.333 | 1.333 | 0.333 | 0
Adder | 0 | 0.5 | 1 | 0.5
Reading it
All 3 multiplies could land in s1 — ASAP would need 3 multipliers.
The multiplier peak (1.33) shows where the pressure is, and where FDS must relieve it.
Notes: Step two builds the distribution graph: spread each operation uniformly over its frame and add up the expected demand per resource type per step. The tall multiplier bars in s1 and s2 are the contention FDS will try to flatten.

## Slide 6
5
STEP 3 — FORCES
Score every candidate placement
Self-force = DG-weighted change in the operation's own probability. Positive ⇒ pushes into a crowded step; negative ⇒ moves toward an idle one.
+0.33
place v3 → s1
into the crowded step — bad
−0.67
place v3 → s3
into an idle step — good
Total force = self-force + predecessor/successor force. Fixing an operation shrinks its neighbours' frames, so the move is scored by its full effect on the schedule.
Notes: Step three is the heart of the method. Each candidate (operation, step) gets a force: the distribution value times how the move changes probabilities. Moving v3 into the busy step 1 scores positive — bad; moving it to the empty step 3 scores negative — good. The total force also folds in the effect on predecessors and successors.

## Slide 7
6
THE ALGORITHM
A constructive, globally-informed loop
1
Compute frames + DG Run ASAP/ALAP, build the distribution graph from current frames.
2
Evaluate all forces Total force for every unscheduled op in every step of its frame.
3
Commit lowest force Fix the single best (op, step) pair — irrevocably.
4
Repeat Tighten neighbours' frames; loop until all ops are scheduled.
Greedy at the outer level — but each decision is informed by the global distribution, not just the current step.
Notes: Putting it together: recompute frames and the distribution graph, score every candidate, commit the lowest-force placement, and repeat. It commits one operation per pass — greedy at that level — but every score reflects the whole graph, which is what separates it from list scheduling.

## Slide 8
7
WORKED EXAMPLE — RESULT
The peak collapses, the latency holds
Chart: Multiplier demand per step
| s1 | s2 | s3 | s4
Initial DG | 1.333 | 1.333 | 0.333 | 0
After FDS | 1 | 1 | 1 | 0
3 → 1
multipliers, same λ = 4
FDS schedule
s1: v2× s2: v1×
s3: v3× , v4+ s4: v5+

## Slide 9
8
IMPLEMENTATION IN C++
The main feature: total-force evaluation
double force(const Problem& p,
const vector<int>& fixed,
int op, int step) {
Frames before = compute_frames(p, fixed);
auto dg = distribution_graph(p, before);
vector<int> trial = fixed; trial[op] = step;
Frames after = compute_frames(p, trial);
double f = 0.0;
// sum over every op whose frame moved
for (each unscheduled u, and op)
for (int s = 1; s <= L; ++s)
f += dg[type(u)][s]
* (P_after(u,s) - P_before(u,s));
return f; // self + pred/succ force
}
Single C++ file, standard library only
Pins a candidate, recomputes all frames
Self + predecessor/successor force fall out of one recomputation
Verified run
first commit v3→s3, force −0.917; multiplier peak 3 → 1
Notes: I implemented the method in portable C++. The main feature is this force routine: it pins a candidate, recomputes every time frame, and sums the distribution-weighted change in probability — so the self-force and the neighbour forces come out of one loop. Running it reproduces the example exactly: first commit v3 to s3 at force minus 0.92, multiplier peak drops three to one.

## Slide 10
9
FROM SCHEDULE TO RTL NETLIST
The output is a netlist of VHDL entities
FSM controller — states S1…S4
Multiplier
(mul_unit)
Adder/ALU
(add_unit)
Registers
r_v1…r_v4
one functional unit = one VHDL entity, shared across steps
State | Operation(s)
S1 | v2 = c × d
S2 | v1 = a × b
S3 | v3 = e × f ∥ v4 = v1 + v2
S4 | v5 = v3 + v4
S3 runs the multiplier and the adder in parallel — distinct resource types, no conflict. Against ASAP's three multipliers, FDS yields a netlist with one.
Notes: The product of HLS isn't the schedule but the netlist it implies: one multiplier, one adder, the registers, and a four-state controller — one state per control step. Each unit is a VHDL entity I wrote. The controller drives the shared units per the schedule; step 3 uses multiplier and adder in parallel.

## Slide 11
10
FDS IN THE SCHEDULING LANDSCAPE
Four methods, three tradeoff axes
Method | Problem solved | Optimality | Decision scope | Cost
ASAP / ALAP | Unconstrained, min latency | Bounds only | Per operation | Very low
List scheduling | Resource-constr., min latency | Heuristic, greedy | Local, one step | Low
ILP | Either, exact | Optimal | Global, exhaustive | Very high (exp.)
Force-directed | Time-constr., min resources | Heuristic, near-optimal | Global balancing | Moderate
Why FDS: when latency is fixed, resources are precious, and the graph is too large for ILP yet large enough that greedy peaks hurt.
Notes: Two axes really separate these. First, which quantity is fixed — list scheduling fixes resources, FDS fixes latency. Second, global versus local — FDS weighs every step through the distribution graph before each move. ILP is optimal but exponential. FDS is the pragmatic middle when latency is fixed and the graph is moderate.

## Slide 12
11
CRITICAL EVALUATION
Strengths, limits, fit, and an extension
Strengths
Principled, instance-specific cost; global view
Extensible & polynomial-time
Limitations
Per-decision recomputation; greedy, no backtracking
Uniform-probability & fixed-delay assumptions
Where it fits
Fixed-rate DSP datapaths (FIR/IIR, transforms)
Poor for control-dominated / very large graphs
Extension (open)
Force as priority in a list scheduler
Conjecture: dependency-aware probability model
Notes: My assessment. Strengths: the force is a principled, global cost, and it's extensible and polynomial. Limitations — and the most fundamental is that it's greedy with no backtracking, plus the uniform-probability assumption. It fits fixed-rate DSP datapaths, not control-dominated designs. As an open direction I'd explore a non-uniform, dependency-aware probability model.

## Slide 13
Conclusion
A deliberate middle ground Global balancing without the exponential cost of exact search.
One idea, carried through Treat the distribution graph as springs and flatten the peaks.
Real resource savings Example: 3 → 1 multiplier at the same latency, realised in VHDL.
Key references: Paulin & Knight, IEEE TCAD 1989 / DAC 1987 · De Micheli 1994 · Teich 1997
Notes: To close: force-directed scheduling is a deliberate middle ground — it gets the global view greedy methods miss, at polynomial cost. One intuition runs through it: balance the distribution graph like springs. On the example it cut multipliers from three to one at the same latency, which I realised as an RTL netlist. Thank you — happy to take questions.